Flow Measurement - Instructional Survey Answers

1.  	Describe the following as they apply to flow measurement:

Reynolds Number - Dimensionless number used to infer flow regime.

High Accuracy - No definite meaning.

Applicable Range - 	Flow rates over which the flowmeter must operate in the 	process.

Ideal Flowmeter - Perfect flowmeter (that does not exist) - Accurate, linear, simple to install, not effected by fluid properties, no cost .

Cavitation -Formation and subsequent implosion of bubbles formed when the liquid pressure falls below and subsequently rises above the liquid 	vapor pressure.  The pressure drop and recovery are caused by the 	restoration of the flowmeter and can damage the flowmeter.

2.  	Which is superior, flowmeter A which has an accuracy of 1/2 percent of full scale or flowmeter B which has an accuracy of 1 percent of rate?

Flowmeter A:  50 - 100% of scale

Flowmeter B:  0-50% of scale

3.	How are the following flowmeters affected by density and viscosity?

| Flowmeter | Density | Viscosity |
| --- | --- | --- |
| Orifice Plate | - 1/2% per % change | RD changes can effect measurement |
| Vortex Shedder | RD changes can effect measurement | RD changes can effect measurement |
| Magnetic | None | None |
| Thermal | Can effect thermal properties | None |
| Positive Displacement | None | Effects slippage |
| Mass | None | None |

4.	List possible causes of the following symptoms.

| Symptom | Possible Causes |
| --- | --- |
| Low flow measurement Control valve wide open | pumping problem; obstruction in control valve |
| Orifice plate Bouncy analog signal | air in impulse line (liquid service) pulsating flow (gas service) |
| Vortex shedder Max. flow confirmed Analog signal at 0% | low temperature increases viscosity causing low RD |

5.	What percentage of flowmeter users are knowledgeable of the compromises necessary for flowmeter selection?

1-3%

6.	What color is the sky?

Depends on time of day and atmospheric conditions.

7.	List some advantages of a mass flowmeter over the following:

Orifice Plate - For mass applications, not effected by density, temp, RD, fewer leak paths.

Vortex Shedder - Not effected by density, temp, RD.

Magnetic Flowmeter -  Not effected by density, temp.

Thermal Flowmeter -  Not effected by temp.

Positive Displacement - Not effected by density, temp.   Fewer moving parts.

8.	List some advantages of the following over a mass flowmeter:

Orifice Plate -   Cost

Vortex Shedder -  Cost

Magnetic Flowmeter - Cost

Thermal Flowmeter - Cost, low pressure gas applications

Positive Displacement - Precise volumetric measurement

9.	Why would a user purchase a mass flowmeter over another flowmeter?

Precise mass flow application; not sure of fluid properties

10.	Why would a user purchase a flowmeter other than a mass flowmeter?

Cost

11.	Which flowmeter does a user buy?

Usually the first one that appears to work.